Graphics Programming
Rendering
Harsh Sarkar

---
Insert pictures to show image formation in human eye (physics) and Mach band effect (psychology).
Introduction
- Rendering is the process of producing realistic pictures. Rendering involves both physics and psychology.
- Illumination is one way of creating realistic pictures. When light falls on a surface, it can be absorbed, reflected or transmitted.
- Illumination models to

---
A diagram to illustrate transmission of light.
Illumination models
- When light falls on a surface, it can be absorbed, reflected or transmitted.
- Some of the incident light is absorbed and converted to heat.
- Another portion of light is absorbed and then re-emitted. It is called diffusely reflected or transmitted light. Transmitted light is scattered equally in all directions, so the viewing angle does not matter. The colour of the object is determined by the nature of the transmitted light.
- Finally, some of the light is reflected directly from the surface. The characteristics of the reflected light is the same as that of the incident light.
- Additionally, an object also receives the light that the surrounding reflects. It is called ambient light.

---
A simple illumination model
- Lambert’s cosine law governs the reflection of light of light from a point source by a perfect diffuser. It states that:
  I(λ) = IL(λ) kd(λ) cos(θ)
- I(λ) the intensity of reflected light. IL(λ) is the intensity of incident light. kd(λ) is called the diffusion function and is a real number value between 0 and 1. θ is the angle between incident light and normal to the surface and thus lies between 0 and π/2.
- Adding ambient light and Lambertian contribution, we obtain the final result:
  I(λ) = Ia(λ) ka(λ) + IL(λ) kd(λ) cos(θ)
- Ia, ka and kd are considered constants for simplicity, so the simplified equation becomes:
  I(λ) = Ia ka + kd IL(λ) cos(θ)